## Slide 1
CorroSight by CorroGuard AI
Intelligent Pipeline Corrosion Prediction and Repair Planning
Predict corrosion. Understand uncertainty. Prioritize action.
Team: [Member 1] · [Member 2] · [Member 3] · [Member 4]
GCEM Hacks 5.0 · Second-round review · 23 October 2026
SYNTHETIC DEMO DATA
Notes: (about 20 seconds) Good evening. We are [team name] and this is CorroSight by CorroGuard AI. Pipeline operators inspect the same pipeline every few years. CorroSight connects those inspections, shows how sure we can be about every change, and explains which findings an engineer should look at first, and why. Everything you will see runs on a fictional, synthetic pipeline. We built it that way on purpose, so we can check our answers against a known truth.

## Slide 2: Which defect is which, seven years later?
JUDGING CRITERION
Problem & Solution · 20
Positions drift between runs
The inspection tool's odometer drifts. Defect T0153 in segment S17 is reported 0.47 m further along in 2023 than in 2016.
Identity is not always clear
29 of 241 pairings have a competing candidate that fits almost as well. Guessing would silently corrupt the growth numbers.
Every measurement has noise
Tool uncertainty is 0.3–0.4 mm (1σ). For 181 of 367 findings the observed change is within that noise.
Data is incomplete
12 errors and 8 warnings in the records; 41 findings miss an engineering input such as wall thickness or pipe grade.
THE QUESTION ENGINEERS ASK
What changed, how sure are we, and what should we look at first — and why?
WHO NEEDS THE ANSWER
Pipeline Integrity Engineer
Inspection Data Analyst
Maintenance & Inspection Planner
Operator / Asset Integrity Manager
Notes: (about 60 seconds) Operators receive in-line inspection reports years apart: here 2016 and 2023 for the same pipeline. To know whether corrosion is growing you must first know which 2023 record is the same defect as which 2016 record. That is harder than it sounds, for four reasons, all taken from our dataset: 1. Positions drift. T0153 appears 0.47 m further along in 2023 purely because the tool's odometer drifted. 2. Identity is sometimes unclear. 29 pairings have a second candidate that fits almost as well. 3. Measurements are noisy. Tool uncertainty is 0.3 to 0.4 mm, so for 181 findings the change could simply be noise. 4. Data is incomplete: 20 errors and warnings, and 41 findings missing an engineering input. Four kinds of people need the answer, and they ask the same question: what changed, how sure are we, and what should we look at first, and why. We are not claiming existing industry tools cannot do any of this; our focus is making the evidence and its uncertainty traceable.

## Slide 3: What each user needs, and the rules we set
JUDGING CRITERION
Problem & Solution · 20
STAKEHOLDER NEEDS
Pipeline Integrity Engineer
The evidence and reason behind each finding, and a place to record the decision
Inspection Data Analyst
Data-quality issues, suspect measurements and uncertain matches, found early
Maintenance & Inspection Planner
Which investigations cover the most uncertainty within a budget
Operator / Asset Integrity Manager
Review progress, open issues and a traceable record for audits
DESIGN PRINCIPLES, FIXED BEFORE WE BUILT
1
Never alter source data
Flag problems; keep every original value
2
Never guess identity
Uncertain matches stay visible and provisional
3
Show uncertainty with every number
And label it observed, calculated or predicted
4
Give every priority a written reason
Named rules, not a black-box score
5
People decide, the system records
Every decision attributed and traceable
Notes: (about 60 seconds) Before writing any code we asked who would use this and what each person needs. The integrity engineer needs the evidence and the reason behind each finding, and a place to record a decision. The data analyst needs data problems and uncertain matches surfaced early. The planner needs to know which investigations cover the most uncertainty within a budget. The operator or manager needs progress, open issues and a traceable record. From that we fixed five design principles that every later decision had to respect: never alter the source data; never guess a defect's identity; show uncertainty with every number and say what kind of number it is; give every priority a written reason; and let people decide while the system records. These principles are the backbone of the design.

## Slide 4: Solution design in four layers
JUDGING CRITERION
Problem & Solution · 20
INPUT
Inspection data
Two or more in-line inspection runs
CSV or Excel listings
Pipe data: wall thickness, grade, pressure
→
ANALYSIS ENGINE
Evidence, step by step
1 Validate records
2 Align runs and match defects
3 Observed change + uncertainty
4 Illustrative forecast
5 Rule-based prioritisation
→
DECISION WORKFLOW
People decide
Review workbench with reasons
Four roles, permission-checked
What-if and planning scenarios
→
EVIDENCE
Traceable record
Evidence Passport (PDF + CSV)
Reproducible snapshots
User-attributed audit trail
EVERY VALUE CARRIES ITS KIND
OBSERVED
CALCULATED
UNCERTAIN
PREDICTED
HUMAN DECISION
Notes: (about 60 seconds) This is the solution design in four layers, left to right. Input: two or more in-line inspection runs as CSV or Excel listings, plus pipe data such as wall thickness, grade and pressure. The analysis engine, in the middle, is five explainable steps: validate the records; align the runs and match defects; calculate the observed change with its uncertainty; produce an illustrative forecast; and prioritise with named rules. The decision workflow is where people come in: a review workbench, four roles with permission checks, and what-if and planning scenarios. The evidence layer keeps the record: an Evidence Passport, reproducible snapshots and a user-attributed audit trail. Running through every layer, each value carries its kind: observed, calculated, uncertain, predicted, or a human decision.

## Slide 5: How we built it: our project process
JUDGING CRITERION
Problem & Solution · 20
01
Understand the domain
How inspection reports record defects, and why comparing runs is hard
02
Define requirements
Stakeholder needs, design principles, and what we will not claim
03
Design data and ground truth
A data schema and a seeded synthetic pipeline with a hidden answer key
04
Build step by step
Validation, matching, growth, priority: each module with its own tests
05
Validate against the truth
Compare with the answer key; switch features off to test their value
06
Add the decision layer
Review workflow, roles, audit trail, Evidence Passport, 3D explanation
Iterative: each module was tested before the next one was built on top of it.
Notes: (about 60 seconds) This is how we worked, in six steps. First we studied the domain: how in-line inspection reports record defects, and why comparing runs is hard. Then we defined requirements: the stakeholders' needs, the five principles, and just as important, what we would not claim, such as failure prediction or safety certification. Third, we designed the data: a schema and a seeded synthetic pipeline with a hidden answer key, including realistic problems like drift, duplicates and missing values. That answer key is what lets us measure ourselves honestly. Fourth, we built step by step: validation, matching, growth, prioritisation, each with its own tests before the next was built on top. Fifth, we validated against the answer key and switched features off to prove their value. Finally we added the decision layer: the review workflow, roles, audit trail, Evidence Passport and a 3D explanation.

## Slide 6: How it works, step by step
JUDGING CRITERION
Innovation & Technical · 20
1
Validate Schema and range checks; records are flagged, never deleted or overwritten
2
Align Per-segment odometer offset from mutual-nearest anchor pairs
3
Match Normalised distance on position, clock and length (not depth); Hungarian one-to-one assignment
4
Hold ambiguity A competing candidate within the margin → pairing stays provisional, no forecast
5
Observed change ΔD and rate; σ = √(u₁² + u₂²); classified against ±2σ noise
6
Forecast Constant-rate central + upper (+2σ) scenario; optional empirical-Bayes shrinkage
7
Prioritise Rules C1–C5 (condition) and E1–E10 (evidence); category = the higher, with written reason
8
Preserve Role-checked review log, reproducible snapshots, Evidence Passport, audit trail
EVERY VALUE CARRIES ITS KIND
Finding T0177, segment S20
OBSERVED
Depth 3.13 mm (2016) → 6.72 mm (2023)
CALCULATED
+3.59 mm over 7.0 yr = +0.513 mm/yr
UNCERTAIN
Rate band 0.370–0.656 mm/yr (±2σ)
PREDICTED
9.28 mm at +5 yr, upper 10.00 mm (illustrative)
HUMAN DECISION
None recorded yet: awaiting an engineer
Python · pandas · SciPy · Streamlit · Plotly · ReportLab · Three.js — open source, runs on a laptop, no external AI service
Notes: (about 75 seconds) Eight steps, each deliberately simple and explainable. Validation flags problems but never edits the data. Alignment estimates each segment's odometer offset from defects that clearly match. Matching uses position, clock and length, deliberately not depth, so growth cannot bias the match, and the Hungarian algorithm guarantees one-to-one pairs. When another candidate fits almost as well, we mark the pair ambiguous and refuse to forecast from it. Change is compared against combined measurement uncertainty, square root of u1 squared plus u2 squared, at two sigma. Forecasts are constant-rate scenarios with an upper case; we also offer an empirical-Bayes shrinkage model. Prioritisation uses named rules, C for condition and E for evidence, so every category has a written reason. On the right is one real finding, T0177, with every value labelled: observed, calculated, uncertain, predicted, and human decision, which is still empty because no engineer has reviewed it. We never mix these up.

## Slide 7: What makes the approach different
JUDGING CRITERION
Innovation & Technical · 20
Uncertainty-first matching
When two pairings fit almost equally well, the match stays provisional instead of being guessed.
Contradiction finder
Instead of one confidence score, it lists where evidence disagrees and what would resolve it.
Models that challenge themselves
Growth methods compete on held-out data, so the method is chosen on evidence.
Evidence labels
Every value is tagged observed, calculated, uncertain, predicted or human decision.
Evidence Passport
One traceable record of data, analysis, reasons and decisions, reproducible from a snapshot.
3D pipeline twin
Shows matches and priorities in space, so non-specialists can follow the reasoning.
Notes: (about 60 seconds) Six ideas make this approach different. Uncertainty-first matching: when two pairings fit almost equally well we do not pick one silently; it stays provisional and visible. A contradiction finder: instead of a single confidence score, the system lists where pieces of evidence disagree and what extra evidence would resolve each case. Models that challenge themselves: several growth methods compete on held-out data, so the forecasting method is chosen on evidence, not preference. Evidence labels on every value, an Evidence Passport that is reproducible from a snapshot, and a 3D pipeline twin that lets people who are not specialists follow the reasoning in space.

## Slide 8: How we prove it works
JUDGING CRITERION
Feasibility & Execution · 10
VALIDATION APPROACH
1
Answer key kept hidden
A seeded synthetic pipeline with known true pairs and growth rates; the analysis never sees it
2
Compare afterwards
Match precision and recall, growth-rate error and uncertainty-interval coverage
3
Switch features off
Ablation tests show what each step adds (for example, alignment)
4
Test every rule
Automated tests for validation, matching, growth, priorities, roles and exports
EARLY RESULTS ON SYNTHETIC DATA
1.000
precision of likely matches (212 of 212)
0.992
of true pairs recovered (241 of 243)
0.042
mm/yr growth-rate error with shrinkage (baseline 0.057)
280
automated tests passing
Our own synthetic data, so these show the method behaves as designed, not real-world accuracy. Real-data evaluation is phase 3 of the plan.
Notes: (about 60 seconds) How do we know it works? We built the test before trusting the tool. We generate a synthetic pipeline with a hidden answer key: the true pairs and true growth rates. The analysis never sees it. Afterwards we compare: match precision and recall, growth-rate error, and whether the uncertainty intervals cover the truth. We also switch features off to measure what each adds; without odometer alignment, for example, false matches appear. And every rule has automated tests. Early results on that synthetic data: every likely match correct, 241 of 243 true pairs recovered, and a growth-rate error of 0.042 mm per year with the shrinkage model. To be clear, this is our own synthetic data, so it shows the method behaves as designed, not real-world accuracy. Real-data evaluation is phase 3 of our plan.

## Slide 9: Feasibility and execution plan
JUDGING CRITERION
Feasibility & Execution · 10
PROOF OF CONCEPT IN PLACE
Laptop + open-source Python; no paid API, no data leaves the machine
CSV import, plus an importer for a public real-world ILI dataset (Mendeley, CC BY 4.0)
Sign-in with hashed passwords, 4 roles, server-side permission checks, audit log
280 automated tests; exact snapshot replay
PDF / CSV Evidence Passport from the same analysis object
EXECUTION PLAN · each phase has an exit check
1
Stabilise the prototype
Freeze v1.0; regression tests stay green
2
Test on controlled data
Seeded drift, ambiguity and noise cases with known answers
3
Evaluate on representative data
Real ILI listings; expert-labelled pairs for precision / recall
4
Domain-expert review
Integrity engineers check thresholds, rules and outputs
5
Controlled pilot
One line, side by side with the current process; log disagreements
6
Production readiness
SSO / MFA, database, encryption, governance, organisational approval
Known gaps: weld-based alignment, tool-bias correction, 3+ run growth. Remaining-strength methods are out of scope.
Notes: (about 60 seconds) Feasibility. On the left is the proof of concept already in place, running on an ordinary laptop: open-source Python, no paid service, and no data leaves the machine. It imports CSV files and has an importer for a public real-world inspection dataset. It has proper sign-in with hashed passwords, four roles with permissions enforced on the server, and an audit log, plus 280 automated tests. On the right is our execution plan, and each phase has a check before we move on: stabilise, test on controlled data with known answers, evaluate on representative real data with expert-labelled pairs, get integrity engineers to review our rules, run a controlled pilot side by side with the current process, and only then address production security, governance and organisational approval. We are explicit about the gaps: weld-based alignment, tool-bias correction and three-plus-run growth are next; remaining-strength calculation is out of scope by design. Real use needs engineering validation and approval.

## Slide 10
From Inspection Data to Traceable Engineering Decisions
Connects evidence across inspection runs
Makes measurement uncertainty visible
Explains why findings are prioritised
Supports, never replaces, human review
Preserves a traceable record of analysis and decisions
“CorroSight does not merely predict or prioritise. It connects inspection evidence, exposes uncertainty, challenges its own analysis and helps engineers make better-informed decisions.”
Thank you · Questions welcome
Notes: (about 30 seconds) To close: CorroSight connects evidence across inspection runs, makes measurement uncertainty visible, explains why each finding is prioritised, supports rather than replaces human review, and keeps a traceable record. In one sentence: CorroSight does not merely predict or prioritise. It connects inspection evidence, exposes uncertainty, challenges its own analysis and helps engineers make better-informed decisions. Thank you. We are happy to take your questions.